## Slide 1: VETERANS Express Lanes
July – 19, 2017

## Slide 2: Approach
Section - 1

## Slide 3: Tampa Bay Regional Planning Model
Model Years:
2010: Base Year
2019: EC (Existing + Committed)
2030: ICA
2040: CA (Cost Affordable)
Veterans Express Way
Approach

## Slide 4: Networks and Assignment Parameters
Networks
  Veterans Expressway for 2020 and 2040 are extracted out from TBRPM
    Starting point for future year projects
    To be consistent with the regional assignment model procedures
    Number of lanes are consistent with the Toll Plan
TBRPM | Initial | Iterative
Speeds | 60 MPH | CGSTSPEED = LI.DISTANCE / (LI.TIME / 60)
Capacity | 2070 | LI.CAPACITY * LI.NUM_LANES * LI.UROADFACTOR / LI.CONFACAMP
Assignment Settings
ODME Enhancement: For Daily ODME application, Capacities are set to 10 hour capacity (CAPACITY * LANES * 10)
Approach

## Slide 5: TBRPM – Assignment Settings
Speeds are coded at 60 MPH
Capacities along Veterans Expressway are set @ 1380 – 2070 vehicles / hour / lane
Approach

## Slide 6
ODME Development
  Initial Subarea OD Tables from TBRPM
  Profile: AADTs from 2020 TEAR and 2040 TRENDS
  Develop ODME procedure with TBRPM assignment and extracted subarea networks, subarea OD seed matrix and profile as control totals
Subarea OD Tables:
AM, MD, PM, EV
ODME : Daily Table
TBRPM: 2019 & 2040
Subarea Network
Profile: TEAR & TREND
Subarea OD Tables: Daily
Approach

## Slide 7
ELTod Application
Describe how eltod is applied (toll links specification, pull links, network speeds, network edits if any, comparison of the extents of the model )
Subarea OD Tables:
AM, MD, PM, EV
ODME : Daily Table
TBRPM: 2019 & 2040
Subarea Network
Profile: TEAR & TREND
Subarea OD Tables: Daily
Approach

## Slide 8: ODME - Validation
Section - 2

## Slide 9: 2040 ODME “Goodness of Fit”
91 – Mainline 71 - Ramps
Further investigation
Very tight convergence
ODME - Validation

## Slide 10: 2040 ODME Stats
ODME - Validation

## Slide 11: 2020 ODME “Goodness of Fit”
See interactive graphic
ODME - Validation
91 – Mainline 71 - Ramps

## Slide 12
Comparison of ODME Estimated volumes to TEAR and TREND AADTS
ODME - Validation

## Slide 13: ELTod v2.2
Section - 2

## Slide 14: Hourly Distributions (AADT) based on March, 2017 counts
ELTOD - Application
Chart: Hourly Distribution
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Southbound | 0.0036831 | 0.002509 | 0.0021244 | 0.0036966 | 0.0093033 | 0.031826 | 0.090634 | 0.10464 | 0.096562 | 0.074382 | 0.064168 | 0.06119 | 0.057895 | 0.051975 | 0.05147 | 0.052849 | 0.052996 | 0.053985 | 0.04617 | 0.031666 | 0.021046 | 0.016878 | 0.011786 | 0.0065702
Northbound | 0.010775 | 0.0058904 | 0.0038535 | 0.0034995 | 0.0038522 | 0.0072213 | 0.019684 | 0.031622 | 0.034008 | 0.037595 | 0.038168 | 0.042753 | 0.048323 | 0.054718 | 0.063818 | 0.088184 | 0.11363 | 0.11173 | 0.091228 | 0.060226 | 0.044802 | 0.036892 | 0.027675 | 0.019858

## Slide 15: ELTod v2.2 vs v2.3
Section - 3

## Slide 16: Overview
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)

## Slide 17: Overview
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)

## Slide 18: Input Question:
No impact on the current runs
112,900 – 22,000 + 9,800 = 100,700 ?

## Slide 19: Model Results
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)

## Slide 20: ICPP vs. Old Policy (LOS-A Pays)
ELTOD - Application

## Slide 21: Model Results
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)

## Slide 22: Hourly Parameters
ELTOD - Application
Chart: Hourly Parameters
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Old | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -1.65 | -1.65 | -1.65 | -2.25 | -2.25 | -2.25 | -2.25 | -2.25 | -1.65 | -1.65 | -1.65 | -3 | -3 | -3 | -3 | -3 | -3
New | -2.6808 | -2.6808 | -2.6808 | -2.6808 | -2.6808 | -2.6808 | -2.0327 | -1.1927 | -1.1927 | -1.1927 | -2.0327 | -1.6407 | -1.6407 | -1.6407 | -2.0327 | -1.1927 | -1.1927 | -1.1927 | -2.0327 | -2.6808 | -2.6808 | -2.6808 | -2.6808 | -2.6808

## Slide 23: Model Results
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)

## Slide 24: Old (LOS-A Pays) vs. New Policy (LOS-A is Free)
ELTOD - Application

## Slide 25: Old vs. New Policy with same, old hourly parameters
2020
2040
Old Policy
New Policy
2020: About 35% increase in EL volume over old policy
2040: only 13% increase in EL volume over old policy
EL Shares: New policy shows a slight increase in EL Share (to Corridor) to 6.8% in 2020 and 7.6% in 2040
LOS-A: Both in 2020 and 2040 all growth in EL vol happens in LOS A.
No impact to LOS B and higher
The share of EL trips decrease in LOS B and C as the total EL vol increase

## Slide 26: Model Results
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)

## Slide 27: Old (LOS-A Pays) vs. New Policy (LOS-A is Free)
ELTOD - Application

## Slide 28: Old vs. New Policy with different hourly parameters
2020
2040
Old Policy
New Policy
2020: About 98% increase in EL volume over old policy
2040: only 57% increase in EL volume over old policy
EL Shares: New policy shows a significant increase in EL Share (to Corridor) to 10 % in 2020 and 2040.
LOS-A:
In 2020 most of the EL trip increase (83%) occurs in LOSA and some (17%) in LOSB.
In 2040 about 73% EL trip increase is in LOSA and another 8% and 19% in LOS B and C respectively .
The share of EL trips decrease in LOS B and C as the total EL vol increase

## Slide 29: Model Results
Input Question:
No impact on the current runs but useful for later discussion. Clarification on the Profile numbers (Inconsistency between Toll Plan/ Existing and Profile ramp location between Anderson Rd and Waters Ave).
Output Results:
Comparison of ICPP and ELToD 2.2 Old Policy results
Comparison of ELToD 2.2 Old Policy results vs. ELToD 2.3 New Policy results
  Old and new policies use same, old hourly parameters
  Old and new policies use different hourly parameters (old and new respectively)
  New policy results comparison with old and new hourly parameters

## Slide 30: New Policy (LOS-A is Free) Old vs. New Hourly Parameters
ELTOD - Application

## Slide 31: Hourly Distributions (AAWDT vs. AADT)
Section - 4

## Slide 32: Hourly Distributions (AADT vs AAWDT)
Chart: Hourly Distribution
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
SB - AADT | 0.0036831 | 0.002509 | 0.0021244 | 0.0036966 | 0.0093033 | 0.031826 | 0.090634 | 0.10464 | 0.096562 | 0.074382 | 0.064168 | 0.06119 | 0.057895 | 0.051975 | 0.05147 | 0.052849 | 0.052996 | 0.053985 | 0.04617 | 0.031666 | 0.021046 | 0.016878 | 0.011786 | 0.0065702
NB - AADT | 0.010775 | 0.0058904 | 0.0038535 | 0.0034995 | 0.0038522 | 0.0072213 | 0.019684 | 0.031622 | 0.034008 | 0.037595 | 0.038168 | 0.042753 | 0.048323 | 0.054718 | 0.063818 | 0.088184 | 0.11363 | 0.11173 | 0.091228 | 0.060226 | 0.044802 | 0.036892 | 0.027675 | 0.019858
SB - AAWDT | 0.00266 | 0.0019319 | 0.0017794 | 0.0036116 | 0.010023 | 0.036732 | 0.10854 | 0.1244 | 0.11016 | 0.07756 | 0.060518 | 0.05371 | 0.049092 | 0.045379 | 0.046893 | 0.048343 | 0.048384 | 0.050559 | 0.042553 | 0.02842 | 0.01867 | 0.014627 | 0.0099329 | 0.0055223
NB - AAWDT | 0.0081156 | 0.0041934 | 0.002592 | 0.0023503 | 0.003494 | 0.0072974 | 0.021133 | 0.033714 | 0.034927 | 0.036644 | 0.035373 | 0.038638 | 0.044769 | 0.050585 | 0.061867 | 0.090576 | 0.12348 | 0.12253 | 0.096338 | 0.060175 | 0.04309 | 0.034999 | 0.025193 | 0.017929

## Slide 33: 2017 Observed vs 2020 Model Est.
Chart: Sugarwood Distribution
NE - AAWDT | 250.6 | 126.2 | 79 | 73 | 112 | 234 | 683 | 1132.6 | 1100.2 | 1123.6 | 1076.8 | 1149.2 | 1334.4 | 1533.2 | 1897.8 | 2783 | 3684.4 | 3830.8 | 3052.4 | 1830.6 | 1326 | 1064.2 | 741.6 | 537.4
SW - AAWDT | 80.8 | 62.6 | 56.4 | 121.6 | 326.2 | 1188 | 3405.4 | 3744.4 | 3312.2 | 2407.6 | 1898.4 | 1684.4 | 1531.8 | 1413 | 1489 | 1594.8 | 1590.6 | 1698 | 1402.2 | 907.6 | 596 | 447.6 | 305.2 | 169
SW 2020 Model | 76 | 55 | 51 | 103 | 286 | 1047 | 3094 | 3546 | 3141 | 2211 | 1725 | 1531 | 1400 | 1294 | 1337 | 1378 | 1379 | 1442 | 1213 | 810 | 532 | 417 | 284 | 157
NE 2020 Model | 231 | 120 | 74 | 67 | 100 | 208 | 603 | 962 | 996 | 1045 | 1009 | 1102 | 1277 | 1443 | 1764 | 2583 | 3521 | 3494 | 2747 | 1716 | 1229 | 998 | 719 | 511
Obs vs Est
2020 Estimated Corridor level volumes are lower than 2017 observed data. Although 2017 observed is only one week AAWDT, it’s still much lower than the TEAR forecast for 2020.

## Slide 34: 2017 Observed vs 2020 Model Est.
Obs vs Est
2020 Estimated Corridor level volumes are lower than 2017 observed data. Although 2017 observed is only one week AAWDT, it’s still much lower than the TEAR forecast for 2020.

## Slide 35: Hourly Parameters (revised)
Section - 5

## Slide 36: Revised Hourly Parameters

## Slide 37: AAWDT: Old (LOS-A Pays) vs. New Policy (LOS-A is Free)
ELTOD - Application
NOT Comparable:
Hourly distributions + hourly parameters should be consistent (one changes the other must change) across base and new models.
The only time these can be different is under a single policy

## Slide 38: Old vs. New Policy with different hourly parameters
2020
2040
Old Policy
New Policy
2020: About 90% increase in EL volume over old policy
2040: only 44% increase in EL volume over old policy
LOS-A:
In 2020 most of the EL trip increase (80%) occurs in LOSA and some (20%) in LOSB.
In 2040 about 50% EL trip increase is in LOSA and another 5% and 45% in LOS B and C respectively .
EL Shares: New policy shows a significant increase in EL Share (to Corridor) to 10 % and 11.6% in 2020 and 2040 respectively.
NOT Comparable:
Hourly distributions + hourly parameters should be consistent (one changes the other must change) across base and new models.
The only time these can be different is under a single policy

## Slide 39: Revised Hourly Parameters Old (LOS-A Pays) vs. New Policy (LOS-A is Free)
ELTOD - Application

## Slide 40: Old vs. New Policy with different hourly parameters
2020
2040
Old Policy
New Policy
2020: About 99% increase in EL volume over old policy
2040: only 51% increase in EL volume over old policy
EL Shares: New policy shows a significant increase in EL Share (to Corridor) to 10.5 % and 12 % in 2020 and 2040 respectively.
NOT Comparable:
Hourly distributions + hourly parameters should be consistent (one changes the other must change) across base and new models.
The only time these can be different is under a single policy

## Slide 41: August 01, 2017
  Model Recap of August 01, results:
  Enhanced ODME (new OD trip table)
  Hourly distribution based on observed data (Mar 2017)
    AADT
    AAWDT
    Revised hourly parameters
  Model enhancements:
  Shoulder hours
  LOS B and C
  High Toll rates

## Slide 42: ICPP vs. Old (LOS-A Pays) with AAWDT Hourly Distributions and revised Parameters
ELTOD - Application

## Slide 43: AAWDT Hourly Distribution + Revised Parameters Old (LOS-A Pays) vs. New Policy (LOS-A is Free)
ELTOD - Application

## Slide 44: Old vs. New Policy with AAWDT and revised parameters
2020
2040
Old Policy
New Policy
2020: About 23% increase in EL volume over old policy
2040: only 10% increase in EL volume over old policy
LOS-A:
In 2020 most of the EL trip increase (80%) occurs in LOSA and some (20%) in LOSB.
In 2040 about 50% EL trip increase is in LOSA and another 5% and 45% in LOS B and C respectively .
EL Shares: New policy shows a slight increase in EL Share (to Corridor) to 10.5 % and 12.6% in 2020 and 2040 respectively.

## Slide 45: Issue #1: Resolve the shoulder hours dips

## Slide 46: Distributions and Hourly Parameters
Issue: The EL shares by hour show dips at two shoulder hours: 10 and 16

## Slide 47: Distributions and Hourly Parameters
Revised Hourly Parameters

## Slide 48: Issue #2: No LOS B and High LOS C
The EL shares for the peak hours are too high (over 20%) which produces EL volumes of ~1500 resulting in VC over 0.8 and that in turn is creating high LOS C volumes as well as high toll rates.

## Slide 49: Level of Service and Hourly Parameters
2020
2040
Old Policy
New Policy
LOS C volumes are much higher than LOS B.

## Slide 50: Issue #3: Toll rates are too high
The EL shares for the peak hours are too high (over 20%) which produces EL volumes of ~1500 resulting in VC over 0.8 and that in turn is creating high LOS C volumes as well as high toll rates.

## Slide 51: High V/C Results = High Toll Rates
73 ₵
19 ₵
19 ₵

## Slide 52: Toll Curve
The toll rate increases from 19 cents to 73 cents between
V/C 0.65 and 0.85. Even more steeper between 0.8 and 0.87 from 34 cents to 77 cents
73 ₵
34 ₵
19 ₵

## Slide 53: Solution to Issues #2 and #3

## Slide 54: Two approaches
Use observed data (15 mins or even more disaggregate data) to split hourly assigned volumes into 3 categories LOS A, LOS B and LOS C.
Adjust Hourly distributions slightly to get overall corridor volumes below ~9666 which is v/c 0.9.

## Slide 55: Adjusted hourly volumes
Peak hour shares were dropped by 0.5% from the observed

## Slide 56: Level of Service and Hourly Parameters
2020
2040
Old Policy
New Policy
LOS C volumes are still higher than LOS B but reasonable

## Slide 57: Estimated toll rates by hours
The toll rates were dropped to 36 cents from 73 cents lowering the v/c to 0.81 from 0.86.

## Slide 58: Old vs New Policy %EL Shares
Southbound EL Shares
Northbound EL Shares