## Slide 1: VETERANS
Scaling Hourly Constants

## Slide 2: Hourly OD Trip Tables: Hourly Factoring vs ODME

## Slide 3: Processed Volume vs Modeled (8:00 AM)
One hour Model Assigned volume is about ~7000 on SB between Hillsborough and Memorial (5900 GL + 850 EL)
Issue:
Processed volumes show ~ 5,400 trips between Hillsborough Avenue and Memorial Hwy where the modeled assignment for one hour (8:00 AM) shows ~7,000 trips

## Slide 4: Processed Volume vs Modeled (8:00 AM)
One hour Model Assigned volume is about ~7000 on SB between Hillsborough and Memorial (5900 GL + 850 EL)
Why are loaded volumes different:
Profile shows 83,600 (NB + SB) and 13% is 8:00 AM shares. This computes to 41,000 Daily SB and 5,434 8:00 AM hourly volumes.
However, the trip tables are ODME’d at daily to match 41,000 (SB) and the trip table is apportioned to hourly factor, which when assigned estimates ~7,000 trips instead of ~5,400.
ODME should be performed at each of the 24 hours

## Slide 5
Toll Constants same as I-95 Express
Assigning Factored Trip Tables

## Slide 6: Hourly (SB) Traffic
Solution:
ODME each hour with control total developed from same profile and hourly distribution.
This should address the inconsistency in the matrix apportion vs actual period distribution.

## Slide 7: Hourly ODME Trip Table: 8:00 AM
One hour Model Assigned volume is about ~4900 on SB (4200 GL + 680 EL)

## Slide 8
Solution:
ODME each hour with control total developed from same profile and hourly distribution.
This gets the .
NOTE:
Only 8:00 AM is ODME’d Trip Table
Need to repeat this for all 24 hour trip tables (time consuming, at least do it for peak hours)
Assigning ODME Trip Tables (8:00 AM OD)

## Slide 9: Assigning ODME Trip Tables (all hours)
ODME each hour:
Assigning ODME trip tables to the network produce more reasonable EL trips (in range of ~500 to ~600) for SB
NB is too high:
The ODME control totals by hour should be rechecked and revised. These seem too high.

## Slide 10: Assigning ODME Trip Tables (Period)
ODME each hour:
Assigning ODME by period trip tables to the network produce more reasonable EL trips (in range of ~400 to ~500) for SB AM
NB is still too high:
The ODME control totals by period produced higher trips but are slightly lower than hourly ODME trips.

## Slide 11: Investigate High EL Trips
By Peak Direction: Issues is more so with NB than SB

## Slide 12: Investigate – SB EL Trips
Peak hour trip assignment
  ODME by hour
Hour 8: AM – peak direction is SB
  Black = Hourly Count
  Blue = Assigned Volume
  Red is VDF and
  N is number of lanes
Ignore NB direction
  Slightly over-assigned but that’s not our focus issue
The two highlighted circles on either ends of SB shows we have right assignment totals
  Shows a congested mainline with v/c ~0.73 – 0.8 between Hillsborough Ave and Memorial Hwy.
  Shows a relatively less congested v/c of 0.65 on mainline between Independence & Memorial -> Hillsborough.

## Slide 13: Investigate – NB EL Trips
Peak hour trip assignment
  ODME by hour
Hour 17: PM – peak direction is NB
  Black = Hourly Count
  Blue = Assigned Volume
  Red is VDF and
  N is number of lanes
Ignore SB direction
  Slightly over-assigned but that’s not our focus issue
The two highlighted circles on either ends of NB shows we have right assignment totals
  Shows a consistent v/c over 0.8 (even 0.9) on the mainline between Independence / Memorial -> Hillsborough.